## Slide 1
MOULDING DIVISION
Performance Analysis
Data Duo Mentoring Programme • Mid-Programme Review
Prepared by Chandra
MSc Business Analytics, Queen's University Belfast
64 injection moulding machines • 22,520 machine-shifts • January – June 2026

## Slide 2
What This Review Covers
A first full analytical pass on the Moulding production data
01
Scale of production
Total output, weight, and material consumption across the period
02
Reading OEE correctly
Why the headline figure understates machine performance — and what the right number is
03
Performance over time
Weekly trend and one significant anomaly needing explanation
04
Machine reliability
Which machines run consistently, and how wide the spread really is
05
Downtime analysis
Where lost time sits, and whether it is concentrated or systemic
06
Insights & next steps
What this means commercially, and what still needs answering
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
2

## Slide 3
The Scale of Production
Moulding division output, January – June 2026
327.7M
Units produced
Across 64 machines and 22,520 machine-shifts
718 t
Material consumed
718,226 kg of polymer across 13 material types
141k
Machine running hours
Alongside 127k hours recorded as stopped time
Putting that in context
Average part weight is just 2.2 grams — this is a high-volume, low-mass operation where small efficiency gains compound quickly
The single highest-output tool (Mould 9510, Valve 1st & 2nd) produced 41.6 million units on its own — 13% of total output
Roughly 63% of output carries a colour additive; the remaining 37% is natural material with no colourant cost attached
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
3

## Slide 4
Reading OEE Correctly
The headline figure and the operational figure answer two different questions
42.2%
OEE across ALL recorded shifts
Includes the 41% of machine-shifts where the machine did not run at all. These record an OEE of zero and pull the average down.
71.6%
OEE on shifts where machines actually ran
The true measure of how well machines perform when they are scheduled and producing. Downtime on these shifts is 10.5%, not 47%.
Why this distinction matters
9,235 of 22,520 machine-shifts (41%) recorded zero running time — these are idle or unscheduled shifts, not underperforming ones
42.2% is a capacity utilisation signal: how much of the available calendar the plant converts into production
71.6% is an operational performance signal: how effectively machines run once started — the number to use for machine comparisons
Both are valid, but they should never be presented interchangeably. All machine rankings in this deck use like-for-like comparisons.
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
4

## Slide 5
Material Consumption
Where the 718 tonnes go — and why unit share and weight share tell different stories
Chart: 
| Standard Block PP | LLDPE | LDPE | Keptial | Novaduran PBT | LLDPE 6301XR | Random PP | PBT
Units produced (millions) | 172.6 | 52.3 | 48.4 | 20.1 | 11.4 | 9.1 | 5.8 | 3.2
Material used (tonnes) | 582.7 | 54.3 | 5.7 | 28.9 | 2.8 | 2.9 | 24.2 | 4.6
What stands out
Standard Block PP dominates both: 53% of units but 81% of material weight
LDPE is the opposite — 15% of units but under 1% of weight, at 0.12g per part
Random PP and PCR Material are the heaviest parts at ~4.1g each
Part weight varies 35-fold across materials, so unit counts alone are a poor proxy for material cost
Commercial implication: material cost tracking should be weight-based, not unit-based. A 1% waste reduction on Standard Block PP is worth roughly as much as eliminating LDPE waste entirely.
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
5

## Slide 6
Performance Over Time
Weekly average OEE across all 64 moulding machines
Chart: Avg OEE %
| Jan 05 | Jan 12 | Jan 19 | Jan 26 | Feb 02 | Feb 09 | Feb 16 | Feb 23 | Mar 02 | Mar 09 | Mar 16 | Mar 23 | Mar 30 | Apr 06 | Apr 13 | Apr 20 | Apr 27 | May 04 | May 11 | May 18 | May 25 | Jun 01 | Jun 08 | Jun 15 | Jun 22
Avg OEE % | 38.9 | 43.5 | 49 | 47.9 | 44.4 | 48.8 | 45.1 | 43 | 44 | 44.6 | 43.4 | 44.1 | 26 | 34.3 | 46.3 | 41.8 | 44.2 | 46.8 | 55.9 | 48.5 | 35.7 | 43.3 | 37.8 | 45 | 38.8
Anomaly — week of 30 March
OEE fell to 26.0%, the lowest week of the period, recovering fully within two weeks. Needs a direct explanation before this period is used in any baseline.
Otherwise: flat, not improving
Excluding the dip, weekly OEE oscillates between 35% and 56% with no upward trend across six months. Performance is stable but stagnant.
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
6

## Slide 7
Machine Reliability
Share of shifts sustaining ≥90% running efficiency — top 15 machines
Chart: 
| MC 42 | MC 64 | MC 63 | MC 33 | MC 57 | MC 26 | MC 38 | MC 7 | MC 5 | MC 31 | MC 4 | MC 40 | MC 56 | MC 21 | MC 1
% of shifts ≥90% efficiency | 63.4 | 63.4 | 65.1 | 66.6 | 67.3 | 67.4 | 67.5 | 67.7 | 69.5 | 72.3 | 74.2 | 75 | 75 | 78 | 86.6
Reading this chart
MC 1 leads the plant, holding ≥90% efficiency on 87% of its shifts
The spread from 1st to 15th is wide — 87% down to 63% — a real, consistent difference rather than noise
This measures consistency, not peak speed: a machine can post a high one-off OEE and still be unreliable week to week
The top performers are the natural place to look for practices worth replicating elsewhere
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
7

## Slide 8
Downtime: The Best-Performing Machines
Stopped time as a share of total tracked time — lowest 16 machines
Chart: 
| MC1 | MC21 | MC56 | MC63 | MC40 | MC4 | MC57 | MC31 | MC5 | MC24 | MC7 | MC26 | MC58 | MC64 | MC38 | MC33
Downtime % | 11.11 | 15.21 | 17.05 | 19.04 | 19.72 | 19.99 | 23.06 | 24.4 | 25.06 | 25.07 | 25.28 | 25.98 | 26.59 | 27.67 | 28.98 | 29.26
The gap between best and worst is enormous
MC1 loses 11% of its tracked time to stoppages. At the other end of the fleet, ten machines lose over 83% — with several above 90%. That is not a performance gap; it suggests those machines are largely idle or unscheduled rather than running badly, and is worth confirming with the business.
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
8

## Slide 9
Is Downtime Concentrated, or Systemic?
Cumulative share of total stopped hours, machines ranked highest to lowest
Chart: Stopped hours
| MC65 | MC12 | MC48 | MC55 | MC25 | MC60 | MC19 | MC43 | MC11 | MC36 | MC44 | MC61 | MC6 | MC32 | MC13
Stopped hours | 4160 | 4042 | 3963 | 3940 | 3887 | 3874 | 3774 | 3566 | 3515 | 3470 | 2851 | 2800 | 2692 | 2605 | 2536
Cumulative % of all downtime | 3.3 | 6.5 | 9.6 | 12.7 | 15.7 | 18.8 | 21.7 | 24.5 | 27.3 | 30 | 32.3 | 34.5 | 36.6 | 38.7 | 40.7
Finding: downtime does not follow the classic 80/20 pattern
It takes 41 of the 64 machines — 64% of the fleet — to account for 80% of total stopped hours. The top 15 machines shown here reach only 41%. Targeting a handful of worst offenders would leave the majority of lost time untouched; the causes are likely scheduling and process-wide rather than machine-specific.
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
9

## Slide 10
Two Further Checks
Shift performance, and how concentrated output is across tooling
Day vs Night shift
42.7%
Day OEE
41.8%
Night OEE
A 0.9 point difference across six months — effectively no shift effect. Output is also near-identical (166M day vs 161M night).
Output concentration
10 moulds = 54% of output
Unlike downtime, production IS concentrated. Mould 9510 (Valve 1st & 2nd) alone produced 41.6M units — 13% of everything made.
Why these two results matter together
No shift effect means staffing patterns and shift-level supervision are not a driver of the OEE gap — that removes one common hypothesis
Concentrated output means a small number of tools carry the commercial load, so reliability on those specific moulds matters disproportionately
Combined: effort is better spent protecting uptime on the highest-volume tooling than on evening out performance between shifts
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
10

## Slide 11
Key Business Insights
The headline OEE understates the plant
42.2% includes 41% idle machine-shifts. On shifts where machines actually ran, OEE is 71.6% and downtime is 10.5%. The real issue is utilisation of available capacity, not machine capability.
Downtime is systemic, not a few bad machines
41 of 64 machines are needed to reach 80% of total stopped hours. A targeted fix on the worst offenders would leave most lost time untouched.
Material cost sits almost entirely in one polymer
Standard Block PP is 53% of units but 81% of material weight. Any waste or scrap initiative should be weighted by mass, not part count.
Shift is not a factor — tooling concentration is
Day and night differ by under one point. But 10 moulds carry 54% of output, so uptime on those specific tools is where commercial risk concentrates.

## Slide 12
Recommendations
Where the evidence points — stated as options for the business, not conclusions
1
Investigate why 41% of machine-shifts are idle
This single factor explains most of the gap between the 42% headline OEE and the 72% operational figure. Is it order volume, scheduling, changeover capacity, or labour availability?
2
Study the top reliability performers, not just the worst
MC1, MC21 and MC56 sustain high efficiency on 75–87% of shifts. Understanding what differs about them is likely cheaper than diagnosing 41 underperformers individually.
3
Weight waste and scrap tracking by material mass
Standard Block PP carries 81% of material weight. A unit-based waste metric will systematically understate where the money actually leaks.
4
Protect uptime on the ten highest-volume moulds
These carry 54% of total output. Prioritising preventative maintenance and tooling spares here has a disproportionate commercial return.
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
12

## Slide 13
Caveats & Next Steps
What is confirmed, what is assumed, and what still needs an answer
Confirmed with the business
OEE is derived from standard vs actual cycle time, cavity efficiency and running efficiency — values above 100% are expected, not errors
"Plan To Run" is unreliable and has been excluded from all analysis
Blank colour values mean natural material with no colourant — not missing data
Open questions
What caused the OEE drop in the week of 30 March?
Are the 41% idle machine-shifts planned (no orders) or unplanned?
MC66 recorded 35 shifts with zero output — is this a new, retired, or mis-recorded machine?
Should machines with near-total downtime be treated as inactive rather than underperforming?
Second half of the programme
Separate idle capacity from operational downtime as distinct measures, so each can be managed on its own terms
Break downtime out by mould and material to test whether specific tooling or polymers drive stoppages
Quantify the output opportunity: what additional volume is available if idle shifts are reduced by 10%?
Extend the same analysis approach to the Assembly division
Move from description to quantified recommendations the business can act on
Moulding Division — Performance Analysis | Data Duo Mentoring, QUB
13